## Slide 1
Electronics
Principles & Applications
Seventh Edition
Charles A. Schuler
©2008 The McGraw-Hill Companies, Inc. All rights reserved.
LT Spice/SwitcherCad III

## Slide 2: LT Spice/SwitcherCad III
A freeware SPICE III circuit simulator written by Mike Engelhardt at Linear Technologies http://www.linear.com/
  SPICE I and SPICE II were written using the FORTRAN programming language. SPICE III was written using the C programming language (U.C. Berkeley, 1985, http://bwrc.eecs.berkeley.edu/Classes/IcBook/SPICE/)
LT Spice was written to support circuit designers who evaluate or use Linear Technology products.
  It includes an extensive library of Linear Technology devices.
It has schematic capture and is much easier to use than traditional text-based SPICE.
  Traditional SPICE requires a text file called a netlist that describes the circuit to be simulated.
  With schematic capture, the user can enter a circuit using schematic symbols and wires via a graphical user interface.

## Slide 3: LT Spice/SwitcherCad III
Is powerful and fast, but is not as intuitive for beginners as simulators such as Multisim
  Requires more knowledge about SPICE directives and terminology
  Has a limited (mostly proprietary) device library
  Has only basic behavioral gates for digital circuits. It is expandable, but this requires knowledge about SPICE and device behavior.
Is worth learning about
  Since it is free, fast, and powerful, it is one of the most widely used circuit simulators at this time.

## Slide 4: You can create circuits with the schematic editor and then analyze them.
Get started by downloading LT Spice/SwitcherCad III from the Linear Technology website:
http://www.linear.com/designtools/software/switchercad.jsp
Although it’s freeware, many professionals consider it to be superior to some commercial simulators.
Install the program on your computer and then run it.

## Slide 5
Choose File and then New Schematic, or hold down
the Control key and then press the “N” key (Ctrl+N).

## Slide 6: Creating a new circuit …
is easier if the grid is active. Click on View and then Show Grid. (Or, you can simply type Ctrl+G)

## Slide 7
Delete tool
It is easy to place grounds and basic components. Click on the desired component and then move the mouse to position it and then left click to place it. You will find that the connectors (square blue boxes above) snap to the nearest grid points. To place another component of the same type, move to the next location and click the left mouse button again. To cancel or quit a component type, click the right mouse button. It is often more time efficient to place all of the resistors, then the capacitors, and so on. Use the scissors (delete tool) to remove components and wires.

## Slide 8
After a component has been selected, it’s easy to rotate it by holding down the Control key and then pressing the R key. Here, D1 was placed first (by left-clicking in the desired location of the schematic) followed by Control-R and then D2 was placed followed by Control-R again and so on.

## Slide 9
Control-E was used here before placing Q2 on the above schematic. Note that Q2 is the mirror image of Q1. Control-E is the mirror command. Control-R and Control-E are keyboard shortcuts. Shortcuts can save a lot of time.
Rotated components
Mirrored components

## Slide 10: The menu command Tools→Control Panel→Drafting Options→Hot Keys allows you to select your own keyboard shortcuts.

## Slide 11
Additional components are available by clicking on the gate symbol or by pressing the F2 key. Suppose you need a voltage source. Choose “voltage” from the component symbol list, place the source on the drawing area with a left click. Right click the source to specify the voltage. To specify an ac voltage source, select Advanced after right clicking.
or

## Slide 12
Specifying a SINE ac voltage source
Amplitude and Frequency
(V1, as shown
here, is currently
a DC source.)

## Slide 13
Use the pencil tool to connect the components. Left click a terminal (blue box) and then move the mouse to the connecting terminal and left click again. The crosshairs below are positioned to connect R4 to R5.
The blue boxes disappear after they are connected.

## Slide 14
Tool Bar
Summary
Place Circuit Element
Draw Wire
Place Ground
Label Node
Place Resistor
Place Capacitor
Place Inductor
Place Diode
Move
Drag
Undo
Redo
Rotate
Mirror
Place Comment
Place SPICE Directive
Zoom In
Pan
Zoom Out
Autoscale
Delete
Duplicate
Paste b/t Schematics
Find
Simulate

## Slide 15
Or, click Select Resistor
to view a Standard list.
Place a resistor.
and right click it.
Enter the values.

## Slide 16
Right click the resistor label to enter a new reference designator. You can specify vertical text.

## Slide 17: Models are required.
Missing models will generate error messages.
  The next slide shows an example.
There are several ways to add models.

## Slide 19: You can expand the component data base.
For example, suppose that you want to simulate a circuit using a BFR540 transistor and that you have the SPICE model saved in text format via Windows Notepad (go to Start, Programs, Accessories to launch this basic text editor).
  Load the SPICE model into Windows Notepad and then Copy it to the clipboard using Control+A followed by Control+C.
  Use Windows Notepad with File Type set to All Files to open the file C:\Program Files\LTC\SWCADIII\lib\cmp\standard.bjt, scroll to the end of that file, and then paste the model from the clipboard (Control+V) and then Save the file.
  The next time that you run LT Spice, the BFR540 will be available as a choice when selecting an NPN BJT transistor as shown on the next slide.

## Slide 21: A SPICE model for the BFR540
.MODEL BFR540 NPN
+ IS = 1.04516E-015
+ BF = 1.84359E+002
+ NF = 9.81774E-001
+ VAF = 4.16981E+001
+ IKF = 1.00000E+001
+ ISE = 2.32436E-013
+ NE = 2.02825E+000
+ BR = 4.39917E+001
+ NR = 9.92532E-001
+ VAR = 2.09773E+000
+ IKR = 1.66296E-001
+ ISC = 1.29849E-016
+ NC = 1.06486E+000
+ RB = 5.00000E+000
+ IRB = 1.00000E-006
+ RBM = 5.00000E+000
+ RE = 3.53552E-001
+ RC = 1.34000E+000
+ EG = 1.11000E+000
+ XTI = 3.00000E+000
+ CJE = 1.97895E-012
+ VJE = 6.00000E-001
+ MJE = 3.32695E-001
+ TF = 7.45719E-012
+ XTF = 1.14072E+001
+ VTF = 3.15854E+000
+ ITF = 1.56917E-001
+ CJC = 7.93745E-013
+ VJC = 1.85522E-001
+ MJC = 8.41656E-002
.ENDS

## Slide 22: A SPICE model can be added directly to the schematic.

## Slide 23: Adding a model to a schematic
Copy the model to the clipboard.
  Left click and hold and drag over the model and then capture it with Control-C. e.g. .MODEL 1N4001 D IS=29.5E-9 RS=73.5E-3 N=1.96 CJO=34.6P VJ=0.627 +M=0.461 BV=60 IBV=10U
Click on .op on the toolbar
Paste the model into the window.
  Control-V.
Click OK.
Place the model on your schematic with a left click.
This method is often preferred when sharing circuits with others.
  The necessary model or models are imbedded in the circuit file.

## Slide 24: Where does one obtain SPICE models?
Search the Internet … many are available as free downloads or can be copied to the clipboard and then pasted into Windows Notepad (or onto your schematic via .op on the toolbar). Some links are provided at the end of this presentation.
Search device manufacturers’ websites.
Modify an existing model.
Create your own.
  Software is available. http://www.intusoft.com/spicemod.htm
Or, you can use a subcircuit.

## Slide 25: Subcircuits (.SBCKT)
Are often used when repetition occurs.
  Better than cluttering the schematic with redundant information
Also can be used to replace a complicated device such as an OP-AMP, a DIAC or a TRIAC.
The next slide shows a common dimmer circuit where the DIAC and TRIAC functions are defined by subcircuits.
  LT Spice has pre-defined schematic symbols for DIACS and TRIACS, but no corresponding models.

## Slide 27: More about models and subcircuits
Models given as .MODEL statements are for intrinsic SPICE devices such as diodes and transistors. The .MODEL statement gives the parameters for the specific component. The general behavior of the device is already known by SPICE; only the parameters need to be given to finish specifying the component's electrical characteristics.
On the other hand, models given by .SUBCKT statements define the modeled component by a collection of intrinsic SPICE devices. For example, the SPICE model of an opamp would be given as a subcircuit. In the previous slide, the SPICE models of a DIAC and a TRIAC were specified as subcircuits.

## Slide 28: LT Spice is useful for analyzing circuits designed by others.
It is sometimes only necessary to use it to review and experiment with circuit files that have already been created.
  Many can be found in the LT Spice subdirectories.
  Some examples are available for download. This is an outstanding example: http://cmosedu.com/cmos1/book.htm

## Slide 29: How to run an existing circuit file
From the File menu, select Open. Make sure the file type is set to Schematics.
Some good examples are available in C:\ProgramFiles\LTC\SwCADIII\examples\Educational (created on your hard drive when you install LT Spice)
Some appropriate examples for the McGraw-Hill basic skills series are available on the website: http://highered.mcgraw-hill.com/sites/0073106941/information_center_view0/
The next slide shows a circuit from Schuler’s book. To view the dc voltages and currents, a dc analysis is selected by first clicking on Simulate, then Edit Simulation Cmd.
  The SPICE directive is .op.

## Slide 31
The DC operating point selection provides all node voltages and device currents.
When you click OK, the SPICE directive .op is placed on the schematic.

## Slide 32
A ground is required for simulation.

## Slide 33
-24V
-12V
40W
28.8W
9.6W
1.2W
12W
-88W
-3.6W
After a DC operating point analysis, moving the cursor over the schematic reveals the various node voltages, currents, and the dissipations in each component. These values are displayed in the lower left portion of the screen.
DC operating point (I(R5) = 200 mA Dissipation = 1.2 W
Placing the cursor here shows the current and the dissipation in R5, as shown below.
Summing the dissipations in this circuit produces zero. The negative signs at V1 and V2 indicate that they are power sources.

## Slide 34: Waveforms
Waveforms are what one sees on an oscillocope (graphs of instantaneous voltages versus time).
Waveforms can be viewed via the transient analysis option. Click on Simulate, Edit Sim Command, and then select the Transient tab.
The next three slides show the procedure.

## Slide 35
Load the circuit from the file menu.
Then, click run.

## Slide 36
Move the cursor to the desired node. When the cursor changes
to a probe, click the left mouse button to view the waveform.
A small differential signal plus a large common-mode signal

## Slide 37
Move the cursor to the collector. Left click and now two waveforms are shown.
Can you see the 60 Hz common-mode component at the collector of Q2?

## Slide 38: The next slide demonstrates the value of simulation when evaluating circuit performance.
The differential amplifier circuit has been improved by adding a stiff current source.
The common-mode rejection ratio is much better.
  The common mode signal cannot be seen in the output.
Circuit simulators make it easy and fun to investigate issues such as this.

## Slide 39
Stiff current source
The 60 Hz common-mode signal is too small to be seen here.

## Slide 40: Remember, waveforms are available via transient analysis.
You must specify the time duration of a transient analysis by specifying a Stop Time.
  Often, this is all that is required.
You can also specify the Time to Start Saving Data.
  Useful in circuits where the start-up period is not important.
You can also specify the Maximum Timestep.

## Slide 41
Go to Simulate and then click on Edit Simulation Cmd.
The time duration of a transient analysis is like choosing the time base setting on an oscilloscope.

## Slide 42
For a basic analysis, this is often all that needs to be specified.

## Slide 43
In this circuit, the common-mode signal is 60 Hz. A 60 Hz signal has a period of roughly 17 milliseconds. Thus, a Stop Time of 20 milliseconds is a reasonable choice.

## Slide 44
Expanded waveform measurements are easy. Hold the left mouse button down and drag a box around the area of interest. Before you release the button, the measurements are available here: dx = 500 uS (2 kHz) dy = 4.7 V
Box

## Slide 45
When you release the mouse button, the area inside the box will be zoomed to fill the waveform display. Restore the original waveform by right-clicking in the waveform area and then selecting Zoom to Fit or press Ctrl+E.

## Slide 46
To obtain an accurate frequency measurement, draw a box around several cycles and then draw a second box to capture one cycle.

## Slide 47
1.572 kHz
This box captures one cycle. The peaks are easier to identify than the zero crossings
The output frequency of this Wien bridge oscillator is predicted by 1/(2πRC), thus we can expect an output at 1.59 kHz.

## Slide 48
To obtain the voltage difference across two nodes, move the cursor to the first node and left click when it changes to a red voltage probe and then without releasing the mouse button, move to the second node and when the cursor changes to a black voltage probe, release the mouse button.

## Slide 49
To determine the Average and RMS values of a waveform, hold down the Control key and left click the waveform’s label.
Ctrl+Left Click here

## Slide 50: The Fourier transform
Converts from the time domain to the frequency domain (the signal spectrum)
  Schuler, 7th edition, page 500
A FFT (fast Fourier transform) is available in LT Spice.
  After a waveform is plotted, right click in the waveform window and select FFT. Choose the node of interest and then click OK. Left click the node label in the FFT window and then use the keyboard arrow keys to make accurate measurements of frequency and amplitude for the various spectral components. Left click and hold to draw a box around a part of the graph to expand it.

## Slide 51
FFT display

## Slide 52
Expanded FFT display
Note: you can increase the simulation time for better FFT resolution.

## Slide 53
Simulation time = 0.1 seconds (better resolution)
Simulation time = 0.01 seconds

## Slide 54: Individual waveforms can be placed onto different plot panes.
Right click in the waveform pane and then select Add Plot Pane.
The next slide shows the usefulness of this feature.
  With all five waveforms on one plot pane, the display is confusing.
  Separate plot panes make it easy to see the divide-by-two action of each flip-flop.

## Slide 56
There are three important waveforms here.
Three plot panes add clarity.
555 one-shot
Input (TRIG)
Threshold waveform
Output

## Slide 57: A dc offset is also available.
The next slide shows a D/A converter.
The input waveforms were separated by right-clicking on the node name, e.g. V(b1), as shown below, and adding a dc offset of = +2 volts.
It also shows how colors can be chosen by using Tools→Color→Preferences→Selected Item→Waveform→Background→Grid→Axis
dc offset
V(b1)+2

## Slide 58
0 dc offset
+2 dc offset
+4 dc offset
+6 dc offset
Separate plot plane

## Slide 59: Current waveforms
Moving the cursor to the inside area of a component, after a transient analysis has been run, displays the current waveform in that component.
When the cursor morphs to a current probe:
  left click to see the current waveform.
This is illustrated in the next slide.

## Slide 60
Current waveforms can be obtained after a transient analysis by moving the cursor to the inside of a device. When the cursor changes to a current probe, left click the mouse to obtain the current waveform.
The current probe, like the voltage probe, shows time variations after a transient analysis. Here, the current in R1 averages 2 mA (which was measured earlier in a dc analysis) and the current fluctuations in R1 are easy to see.
Current probe icon

## Slide 61
The current in Q1 is constant.
The constant current source is doing its job!

## Slide 62
To display a power waveform (instantaneous power), hold down the Alt key and left click on the component of interest (after the cursor has changed to a thermometer).
e.g., Alt+click here.

## Slide 63
To determine the average power dissipation, Control+left click on the label.

## Slide 64: AC Analysis
Provides the frequency response of a circuit.
  Both the amplitude and the phase angle are graphed as a function of frequency (Bode plot).
Go to Simulate, Edit Simulation CMD, and then click on the AC Analysis tab.
  You must enter the Number of points per sweep interval, the Start Frequency and a Stop Frequency.
  You can also choose various sweep intervals.
    Octave, Decade, or Linear

## Slide 65
Output
Input
AC Analysis provides the frequency response of a circuit. One of the signal sources must be designated as the input by specifying an AC Amplitude for Small signal AC analysis. Run the simulation and then probe the output for the Bode plot.

## Slide 66
Ctrl-left click the label
to measure bandwidth.

## Slide 67
Here, the only change is the transistors. This illustrates the need for proper SPICE models when investigating issues such as bandwidth. The BFR540 is a high-frequency transistor.
BFR540
2N3904

## Slide 68: Configuring LT Spice
There are many user options.
  SPICE options (e.g. integration method)
  Drafting options including font properties
  Data saving defaults
  Compression
  Most options are available via a control panel.
The next two slides illustrate some configuration choices.

## Slide 69
Tools  Control Panel  Operation
LT Spice generates several kinds of files. To save disk space and avoid clutter, these files can be deleted automatically.

## Slide 70
Tools  Color Preferences
LT Spice allows color choices for waveform plots and the background on which they are plotted. Also, the axes and grid colors are selectable

## Slide 71: Support for LT Spice
The next slide shows an example of the built-in help system.
The help file is a downloadable and printable document: http://ltspice.linear.com/software/scad3.pdf
There are numerous other resources. Check the Links slide at the end of this presentation.

## Slide 72
Press F1 for the Help System. You can download the User’s Manual from: http://ltspice.linear.com/software/scad3.pdf

## Slide 73
The help files explain many things: for example, how to model transformers.

## Slide 74: Some “gotchas” and hints
“M” and “m” are interpreted the same by SPICE. Thus, a resistor value of 10M is the same as 10m (ten milliohms or 10-3).
  Use 10MEG (or 10E6) to specify ten megohms.
Do not enter “1F” or “1f” as the capacitance for a one-farad capacitor (enter “1”). “F” and “f” designate the prefix femto (10-15).
SPICE will not allow voltage sources in parallel, even when of the same value.
  Add series resistances.
SPICE will not allow current sources in series, even when of the same value.
  Add parallel resistances.

## Slide 75: Prefixes are case insensitive: T = t, G = g, and so on
T = terra = 1012
G = giga = 109
MEG = meg = 106
K = kilo = 103
M = milli = 10-3
U = micro = 10-6
N = nano = 10-9
P = pico = 10-12
F = femto = 10-15

## Slide 76: LT Spice element names
C capacitor
CSW current controlled switch
D diode
E voltage-controlled voltage source
F current-controlled current source
G voltage-controlled current source
H current-controlled voltage source
I independent current source
J JFET
K coefficient of magnetic coupling
L inductor
LTRA lossy transmission line
M MOSFET
NJF N-channel JFET
NMOS N-channel MOSFET
NPN bipolar transistor
PMOS P-channel MOSFET
PNP bipolar transistor
PJF P-channel JFET
Q BJT
R resistor
SW voltage controlled switch
T transmission line
V independent voltage source

## Slide 77: LT Spice/SwitcherCad III final notes
Like many modern software tools
  it is relatively easy to begin using but one must spend some time to discover and then master the most powerful features.
As freeware goes, it is outstanding!
  It is relatively bug-free.
  It is compact and very fast.
  It is regularly updated.
A tip for students:
  Knowing how to use a professional level circuit simulator looks great on your resume!

## Slide 78: Links
http://www.intusoft.com/models.htm#freemodels
http://www.penzar.com/links.htm
http://ee.cleversoul.com/simulation.html
http://www.cadence.com/orcad/index.html
http://cmosedu.com/videos/videos.htm
http://cmosedu.com/cmos1/book.htm
http://www.anasoft.co.uk/Spice3F5Manual.html
http://www.onsemi.com/site/support/models
http://www.coilcraft.com/modelsswcad.cfm
http://tech.groups.yahoo.com/group/LTspice/